## Slide 1
Università della Calabria
Dipartimento di Ingegneria Informatica, Modellistica, Elettronica e Sistemistica
Master’s Degree in Electronic Engineering
SOC Estimation Using the Feed-Forward Learning Approach and Machine Learning Techniques with Explainable Artificial Intelligence
Prof. Marco Ricci
Giorgio Ubbriaco
A.Y. 2023-2024
________________________________________________________________________________________

## Slide 2: Access to GitHub Repository
  You can find the full project repository on GitHub at the following link:
  github.com/gubbriaco/soc-estimation.git
  If you experience any issues accessing the repository through the above link, please try the alternative link below:
  nbviewer.org/github/gubbriaco/soc-estimation/tree/master/

## Slide 3: Bibliography
  Shahriar, S.M.; Bhuiyan, E.A.; Nahiduzzaman, M.; Ahsan, M.; Haider, J. State of Charge Estimation for Electric Vehicle Battery Management Systems Using the Hybrid Recurrent Learning Approach with Explainable Artificial Intelligence. Energies 2022, 15, 8003.
  Kollmeyer, Philip; Vidal, Carlos; Naguib, Mina; Skells, Michael (2020), “LG 18650HG2 Li-ion Battery Data and Example Deep Neural Network xEV SOC Estimator Script”, Mendeley Data, V3.
  Chen, Zheng & Zhao, Hongqian & Shu, Xing & Zhang, Yuanjian & Shen, Jiangwei & Liu, Yonggang. (2021). Synthetic Stage of Charge Estimation for Lithium-ion Batteries Based on Long Short-Term Memory Network Modeling and Adaptive H-Infinity Filter.

## Slide 4: Table of contents
  Abstract
  An overview on the main topics
  Typical approaches and their drawbacks
  Advanced approaches
  Data collection and analysis
  Deep learning techniques
  Machine learning techiques
  Kalman filter
  Observed and predicted SOC values from the test data
  Metrics of the models
  Explaining the FNN model with Explainable AI

## Slide 5: Abstract
  Accurate SOC estimation.
  Estimation SOC remains a challenge.
  In this work, both theory-based methods and advanced approaches based on ML and DL were analized for State of Charge (SOC) estimation.
Notes:   Accurate SOC estimation is essential and crucial to improve operation safety and service life of Li-ion batteries.
  Estimation SOC remains a challenge, leading to the replacement of traditional theory-based methods with data-driven approaches, enabled by increased battery data and AI advancements.
  In this work, both theory-based methods and advanced approaches based on ML and DL were analized for State of Charge (SOC) estimation.

## Slide 6: An overview on the main topics
  What’s SOC and DOD?
  What’s Battery Management System and why is it so important?
  Battery pack, modules and cells.
  Lithium-ion cells.
Notes: State of charge (SoC) quantifies the remaining capacity available in a battery at a given time and in relation to a given state of ageing. It is usually expressed as percentage (0% = empty; 100% = full). An alternative form of the same measure is the Depth of Discharge (DoD), calculated as 1 − SoC (100% = empty; 0% = full).
One important subsystem that can be found inside an electric vehicle is the Battery Management System (BMS). It is an embedded system that is designed to properly manage the particular Energy Storage device, which is typically a rechargeable battery, that is adopted as a source of energy for the entire vehicle. The main tasks that the BMS has to perform are:
• continuously monitor the battery by acquiring measures of voltage, current and temperature
  • compute parameters that describe the state of the battery like the State of Charge (SoC) and the State of Health (SoH)
  • ensure the safety by guaranteeing that every operation performed on the battery lies in the Safe Operation Area (SOA), so by avoiding: over-charge, overdischarge, over-voltage (during charge) and thermal runaway
The battery pack represents the energy storage device of an electric vehicle and is used to stock energy (typically in the form of electrochemical potential) with the purpose of providing it to the vehicle motor and other subsystems. It is managed by the BMS. Modules embed some electronics that help the BMS to monitor the state of the cells by acquiring measures of voltage, current and temperature thanks to the presence of corresponding sensors. In this context the BMS is able to act a control action in order to ensure the safety of the charge/discharge operations performed over the cells and to control the temperature thanks to the presence of a cooling/heating system.
Lithium-ion battery is a particular kind of electrochemical cell that converts electric energy into chemical energy during discharging processs (in this case is called electrolytic cell) and vice versa during charging process (in this case is called galvanic cell). At the simplest abstraction level, the cell is composed by a positive (anode) and negative (chathode) electrodes (active elements) and an electrolyte (passive element). The mechanisms of energy conversion, during charging and discharging processes happen through redox reactions (oxidation and reduction) at the active components. In these circumstances, electrons migrate from one electrode to the other by following an external circuit, while generated ions passes through the electrolyte reaching the other side electrode. The main components of the electrochemical cell from the perspective of a Lithium-ion cell are the following:
    • electrodes: Conductive materials that enable electron and ion movement. The anode stores ions and donates electrons (typically made of graphene), while the cathode accepts electrons and stores lithium by combining it with metal oxides like Co, Ni, Fe, Mn.
    • electrolytes: A medium (liquid or polymeric) that carries ions between electrodes. It typically consists of salts dissolved in solvents, with high ionic conductivity.
    • current collector: A porous material used with liquid electrolytes to prevent electrode contact, thus avoiding short circuits.
    • casing: An external enclosure, typically plastic or metallic, that insulates and protects the cell, preventing electrolyte evaporation and ensuring structural integrity. It can be cylindrical or prismatic in shape.

## Slide 7: Typical approaches and their drawbacks
Open Circuit Voltage Method
Coulomb Counting Method
Modified Coulomb Counting Method
Notes: Open Circuit Voltage Method: SOC(t) is the SOC of the battery at t, a0 is the battery terminal voltage when SOC = 0%, and a1 is obtained from knowing the value of a0 and VOC(t) at SOC = 100%. The OCV method based on the OCV of batteries is proportional to the SOC when they are disconnected from the loads for a period longer than two hours. However, such a long disconnection time may be too long to be implemented for battery. Unlike the lead-acid battery, the Li-ion battery does not have a linear relationship between the OCV and SOC. The relationship between the OCV and SOC cannot be exactly the same for all batteries.
Coulomb Counting Method: The Coulomb counting method measures the discharging current of a battery and integrates the discharging current over time in order to estimate SOC. Coulomb counting method is done to estimate the SOC(t), which is estimated from the discharging current, I(t), and previously estimated SOC values, SOC(t − 1). But there are several factors that affect the accuracy of Coulomb counting method including temperature, battery history, discharge current, and cycle life.
Modified Coulomb Counting Method: To improve the Coulomb counting method, a new technique called modified Coulomb counting method is proposed. The modified Coulomb counting method uses the corrected current to improve the accuracy of estimation. The corrected current is the function of discharging current. There is a quadratic relationship between the corrected current and discharging current of battery. k2, k1 and k0 are constant values obtained from the practice experimental data. The experimental results show that the accuracy of the modified Coulomb counting method is superior to the conventional Coulomb counting method.

## Slide 8: Advanced approaches
  State of Charge Estimation for Electric Vehicle Battery Management Systems Using the Hybrid Recurrent Learning Approach with Explainable Artificial Intelligence: https://doi.org/10.3390/en15218003
  Synthetic Stage of Charge Estimation for Lithium-ion Batteries Based on Long Short-Term Memory Network Modeling and Adaptive H-Infinity Filter: https://doi.org/10.1016/j.energy.2021.120630

## Slide 9: State of Charge Estimation for Electric Vehicle Battery Management Systems Using the Hybrid Recurrent Learning Approach with Explainable Artificial Intelligence
  Dataset: https://doi.org/10.17632/cp3473x7xv.3
Notes: The main objective of this work is to propose an optimized deep learning approach to estimate the SOC and explain the model with the explainable AI.
Collect and preprocess the data for the model training.
5 DL model architectures, based on CNN and RNN, were built to estimate the SOC of the EV battery in an optimum way.
Training of these 5 models with training data and verified with testing data.
Comparison among these 5 models.
Choosing of an optimum model.
Comparison between optimum model and existing state-of-art models.
Explanation of the optimum model via explainable AI.

## Slide 10: State of Charge Estimation for Electric Vehicle Battery Management Systems Using the Hybrid Recurrent Learning Approach with Explainable Artificial Intelligence
The Long Short-Time Memory is developed to prevent the problem of long-term dependency.
The Gated Recurrent Unit is developed as an updated version of LSTM to counteract the complexity of the latter.
Notes: The LSTM is developed to prevent the problem of long-term dependency. It is its default behavior to remember information for long periods of time. is denoted as the cell memory where is denoted as time. The LSTM has 3 gates: forget, input and output. The forget gate decides which information has to be erased from the cell memory. Mainly the sigmoid function decides whether the information in has to be erased or not. are weights metrics, is the previous layer hidden state layer, the is input vector and are the bias of the network. is the input gate and it keeps the new information in the unit memory . Specifically, in the input gate there is a sigmoid layer to choose which value should be updated first. The tanh layer generates the vector of the new candidate values that could be added to the state. Combining , and equations, it is possible to update unit memory . In particular, the output is provided by , which is used to perform the task related to which part of the unit memory will be used, and by where is multiplied with a tanh function which makes values from -1 to 1.
The GRU is developed as an updated version of LSTM to reduce complexity and to work even with small datasets. Specifically, this unit introduce the reset gate and the update gate. The reset gate controls how to integrate a new input with prior inputs in its memory, while the update gate specifies how much of the previous memory should be retained.
The LSTM is developed to prevent the problem of long-term dependency. It is its default behavior to remember information for long periods of time. 𝒄_𝒌 is denoted as the cell memory where 𝑘 is denoted as time. The LSTM has 3 gates: forget, input and output. The forget gate 𝒇_𝒌 decides which information has to be erased from the cell memory. Mainly the sigmoid function decides whether the information in 𝑐_(𝑘−1) has to be erased or not. 𝒘_𝒇 are weights metrics, 𝒉_(𝒌−𝟏) is the previous layer hidden state layer, 𝒙_𝒌 the is input vector and 𝒃_𝒇 are the bias of the network. 𝒊_𝒌 is the input gate and it keeps the new information in the unit memory 𝑐_𝑘. Specifically, in the input gate there is a sigmoid layer to choose which value should be updated first. The tanh layer generates the (𝑐_𝑘 ) ̌ vector of the new candidate values that could be added to the state. Combining 𝑓_𝑘, 𝑖_𝑘 and (𝑐_𝑘 ) ̌ equations, it is possible to update unit memory 𝑐_𝑘. In particular, the output is provided by O_𝑘, which is used to perform the task related to which part of the unit memory will be used, and by ℎ_𝑘 where 𝑂_𝑘 is multiplied with a tanh function which makes values from -1 to 1.
The GRU is developed as an updated version of LSTM to reduce complexity and to work even with small datasets. Specifically, this unit introduce the reset gate and the update gate. The reset gate 𝒓_𝒌 controls how to integrate a new input with prior inputs in its memory, while the update gate 𝒛_𝒌 specifies how much of the previous memory should be retained.

## Slide 11: State of Charge Estimation for Electric Vehicle Battery Management Systems Using the Hybrid Recurrent Learning Approach with Explainable Artificial Intelligence
LSTM
no_params: 9,513,729
CNN-LSTM
no_params: 9,774,849
CNN-Bi-Directional LSTM
no_params: 22,101,761
GRU
no_params: 1,729,217
Hybrid CNN-GRU-LSTM
no_params: 925,313
Notes: LSTM: LSTM is used because of its unique ability to disingenuously recognize sequences over extended periods of time.
CNN-LSTM: CNN is used for the extraction of features on the input data and merged then with the LSTMs.
CNN-Bi-Directional LSTM: A Bi-Directional LSTM is a sequential computational framework that consists of 2 LSTM, one of which receives the input in forward time order and the other receives the input in backward time order. The other parts of architecture are the same of the previous.
GRU: GRU is used because of a less number of gates (than LSTM) and so for its less complexity (than LSTM).
Hybrid CNN-GRU-LSTM: Hybrid model is important to include the prevention from long-term dependency of LSTM, the feature extraction of CNN and the less complexity of GRU.

## Slide 12: State of Charge Estimation for Electric Vehicle Battery Management Systems Using the Hybrid Recurrent Learning Approach with Explainable Artificial Intelligence
The CNN Bi-LSTM model provided the most accurate SOC predictions but had the highest prediction time and number of trainable parameters. In contrast, the Hybrid CNN-GRU-LSTM model achieved similar accuracy to CNN-LSTM but with fewer trainable parameters and less prediction time, making it the optimal model among the five tested.

## Slide 13: State of Charge Estimation for Electric Vehicle Battery Management Systems Using the Hybrid Recurrent Learning Approach with Explainable Artificial Intelligence
Considering the Hybrid CNN-GRU-LSTM model…
Notes: At first, the model that was trained with the data altogether, was tested with SHAP, which revealed that, from the five inputs, the average voltage was the most important input feature. The prediction of the SOC depends on the average voltage the most and on the nonlinear behavior of the battery voltage. Since the average voltage is the average of the voltages (the present voltage and the previous voltage values) of a moving window, which is a statistical method to quickly identify the changes in the residual mean value and standard deviation, it contains a lot of information on the previous condition of the SOC. It is the main requirement of the RNN, that the previous important input and output, should be considered for the present output. Following the average voltage, the present voltage is another important input feature. As the average voltage contains information about the previous and present states altogether, the instantaneous voltage information is also an important feature for the SOC estimation. Furthermore, the average current containing the information on the present and previous loads on the battery, is also important information for the SOC estimation. As the battery behavior changes with the ambient temperature, its importance is shown in the SHAP chart. The instantaneous current was shown to be a less important feature, as its impact was very low in the SOC estimation.

## Slide 14: Synthetic Stage of Charge Estimation for Lithium-ion Batteries Based on Long Short-Term Memory Network Modeling and Adaptive H-Infinity Filter

## Slide 15: Data collection and analysis

## Slide 16: Deep Learning Techniques

## Slide 17: Machine Learning Techniques

## Slide 18: Kalman filter

## Slide 19: Observed and predicted SOC values from the test data

## Slide 20: Metrics of the models

## Slide 21: Explaining the FNN model with Explainable AI

## Slide 22
Thanks.